## Slide 1: UVa Program for common (eRD6 / eRD3) generic detector R&D for EIC Forward Tracker GEMs
Kondo Gnanvo
EIC Weekly Meeting, May 02, 2016

## Slide 2: R&D Program @ UVa: Overall plans
Forward GEM detectors
  Complete the study of stereo-angle (U-V) 2D readout strips
  Zebra connectors + adapter: No connectors mounted on detector ⇨ all FE contacts on outer radius side
  Pursue the study of new assembly technique ⇨ with O-ring and light and strong material bolts ...
R&D on GEM like structures
  Pursue the study of Thin Chromium Cr-GEM ⇨ test performances in high rate, long term stability etc ...
  Test new GEM-like structures such as resistive m-well detectors ⇨ basic performances on small 10x10 prototypes
Front-end Electronics for EIC FT GEMs
  Study performance of VMM electronic (ideally with VMM3 chip) with application for large FT GEM for EIC
  Interface the VMM3 electronic with SRS readout system and DAQ currently used for APV25 at UVa
Funding request for the remaining 2 cycles
  Support for UG students [5 K$]
  Materials: [35 K$]
    GEM parts & accessories: readout board + frames [18 K$] + accessories [2 K$] (current cycle, July 2016)
    Electronics: VMM FE cards + SRS components [10 K$] (next cycle, July 2017)
    New structures: thin Cr-GEM foils and resistive m-well [5 K$] (next cycle, July 2017)
  Travel support [6 K$]

## Slide 3: R&D Program @ UVa: Tentative timeline
July – December 2016
  Acquire small (10 cm x 10 cm) U-V readout board with zebra connection scheme
  Finalize the design and place the order of the full size readout board, Zebra adapter card
  Investigate alternative options for GEM frames and finalize the design for new assembly technique
  Continue work with thin Cr-GEMs
January – June 2017
  Build 1-m long prototype with the common GEM foil
  Acquire a few samples of VMM chip electronic for test with GEMs and set it up the SRS readout
  Prepare for a test beam campaign (at FNAL second half of the year)
  Continue work with thin Cr-GEMs
July – December 2017
  Test the prototype in FNAL test beam, ideally together with the Florida Tech and Temple U. groups
  Test thin Cr-GEM and resistive m-well detector in FNAL test beam.
  Analyse data from test beams, present the results at conference ( like IEEE-NSS) and publish in peer-review paper
  Generic R&D for forward tracker will be considered completed at this point.